Guide to Coherence Training with the BrainMaster

This guide explains how to set up and train coherence using the BrainMaster with 1.9A or later software.  While the BrainMaster contains a complete protocol processor that manages the enhances and inhibits for up to 8 components for each EEG channel, the coherence subsystem has been designed to operate separately, in order to keep things simple.  The coherence training system is basically a form of sound feedback, and does not interact with the protocol processor.  Therefore, it is set up in a different manner, and can be used along with a standard protocol, or by itself.

The key to setting up for coherence training is the following:

On the Display Options dialog:

- Select the components for which you wish to hear sounds

- (optionally) Select the coherence display

On the Feedback Control dialog:

- Select coherence sounds

- Select an appropriate coherence threshold

- Select whether to “uptrain” or “downtrain” coherence

You will hear coherence sounds for any components that were selected.  You can modify these selections from the training screen toggle buttons, if you wish to add or delete components from being heard.  In order to see the choices change, it is helpful to be watching the filtered waveforms or the thermometer window, to see the components come and go as they are selected or deselected.  Once this is done, you do not need to keep any windows visible, for the sounds to be heard.  The coherence sounds will be heard regardless of what screens the user is viewing.

A component will play its coherence sound when its coherence goes above (if uptraining) or below (if downtraining) the coherence threshold.

Adjust the coherence threshold so that the trainee gets useful sound feedback.  It is best if the trained component plays sounds more than half the time, but not all of the time.  The coherence threshold can be raised at any time by typing “c” while the training screen is the active window.  The letter “C” will lower the coherence threshold.

Note that the coherence window is always available whenever 2-channel training is being done, so that it can be viewed at any time, regardless of the type of training being used. Thus, even if you are doing C3 beta/C4 smr training, you can bring up the coherence screen and see the coherence values.  In addition, coherence is always written to the summary file, and to the excel file.  Therefore, you can monitor and look at the coherence between any pair of channels, regardless of how the EEG training is being done.