Demonstrations of protocol design “DC and SCP Training Monopolar 4 Chan”

Records 4 channels of full EEG and DC potentials.  Event Wizard is used to access DC potentials, and compute baseline levels and changes.

Provides MIDI instrument sound feedback when any channel DC rises.  This provides directional training, rewarding DC formoving in  a specific direction.

Provides point and gong feedback whenever the sum of channels rises above a set level for a preset sustained reward criterion (SRC).  This also provides directional training, thus rewarding specifically “surface positive” or “surface negative.”

The 4 channels of DC/SCP are shown in blue, yellow, green, and red in the Event Wizard Window.  These can match the colors of the cables used with the 4-channel connection as follows:

Chan 1 active:  blue

Chan 2 active: yellow

Chan 3 active: green

Chan 4 active: red

The sum of the 4 channels of DC/SCP is shown in white.

There is also  a component band named UltraDelta that is set for 0.01 to 0.1 Hz.  This can be used with the protocol processor or the Event Wizard to provide training on this component for 4 channels.  This would typically be “bidirectional” training.

Example Screen with EEG

Initial test with leads shorted.  Observe points and rewards come when DC is rising.